# GLOSSARY

ABANDONED - When referring to an underground storage tank installation, means out of service and not safeguarded in compliance with the City Code. However, an underground storage tank installation shall not be deemed to be abandoned within the meaning of the City Code if it was closed previously in accordance with this ordinance or any other applicable state, federal or local laws or regulations.

ACCEPTABLE OUTLET - That point where stormwater runoff can be released into a watercourse or drainageway of adequate capacity without causing scour or erosion.

ALLUVIAL FAN - A sloping, fan-shaped mass of sediment deposited by a stream where it emerges from an upland onto a plain.

ALLUVIUM - A general term for all detrimental material deposited or in transit by streams, including gravel, sand, silt, clay and all variations and mixtures of these. Unless otherwise noted, alluvium is unconsolidated.

ALTERATIONS - Cutting, filling, widening, bypassing, channelizing, stabilizing or clearing vegetation in a floodplain.

ANGLE OF REPOSE -The angle between the horizontal and the maximum slope that a soil assumes through natural processes.

ANNUAL -A plant that lives and grows for only one (1) year or season, during which the life cycle is completed.

ANTISEEP COLLAR - An impermeable diaphragm, usually of sheet metal or concrete, constructed at intervals within the zone of saturation along the conduit of a principal spillway to increase the seepage length along the conduit and thereby prevent piping or seepage along the conduit.

ANTIVORTEX DEVICE - A device, usually a vertical or a horizontal plate, carefully designed and placed at the entrance of a pipe to prevent the formation of a vortex in the water at the pipe entrance.

APRON - A floor or lining to protect a surface from erosion; for example, for the pavement below chutes, spillways or at the toes of dams.

ASPECT - The direction a slope faces is a physiographic feature on steep slopes which influences plant growth and adaptation.

ASPHALT

a.     Cutback - Asphalt thinned with lighter hydrocarbons, such as kerosene or naptha.

b.     Emulsion - An emulsion of water and asphalt.

c.     Liquid - (In this application) asphalt which has a sufficiently low viscosity to be sprayed without thinning.

ATTERBERG LIMITS - Soil properties measured for soil materials the Number 40 sieve.

a.     Liquid Limit - The water content corresponding to the arbitrary limit between the liquid and plastic states of consistency of a soil.

b.     Plastic Limit - The water content corresponding to an arbitrary limit between the plastic and semisolid states of consistency of a soil.

c. Plasticity Index - The numerical difference between the liquid limit and the plastic limit.

BARREL  - The usually mildly sloping closed conduit used to convey water under or through a dam; part of a principal spillway.

BASE FLOW  - The stream discharge from ground water accretion.

BEDLOAD - The sediment that moves by sliding, rolling or bounding on or very near the stream bed; sediment moved mainly by tractive or gravitational forces or both, but at velocities less than the surrounding flow.

BERM - A shelf that breaks the continuity of a slope.

BLIND DRAIN - A type of drain consisting of an excavated trench refilled with previous material, such as coarse sand, gravel or crushed stone, through whose voids water percolates and flows to an outlet. Often referred to as a French drain because of its initial development and widespread use in France.

BUFFER AREA - A landscape area on a lot, situated between all street views and all vehicles, structures and areas to be buffered from those views.

BUFFERING - The use of landscaping (other than mere grass on flat terrain) or the use of landscaping along with berms, walls or decorative fences that at least partially and periodically obstruct the view from the street, in a continuous manner, of vehicular use areas, parking lots and their parked cars and detention ponds.

CALIPER - The diameter of an installed tree measured six (6) inches above ground level for small trees (four (4) inches diameter or less) at time of planting; measured at 12 inches above ground level for large trees (greater than four (4) inches diameter). (See Figure 3-1 in Appendix V of this manual) The caliper of installed multi-stemmed trees is determined by adding the full diameter of the largest stem to half the diameter of each additional stem.

CANOPY COVER - That geographic area covered by the vertical projection of the drip line or outer branches of a tree or group of trees in a woodland tract, which may be measured directly from aerial photography and/or measured for all trees at least 30 feet in height.

CATCHMENT AREA - The area, defined by topographic relief, which drains to a point recharge or critical environmental feature.

CAVE - A natural underground cavity, recess, chamber or series of chambers generally produced by the solution of limestone by subterranean water.

CHANNEL - An existing natural water course or a manmade water course designed to meet specifications contained in the City of Austin Drainage Criteria Manual.

CHANNEL  - A natural stream that conveys water; a ditch and channel excavated for the flow of water.

CHANNEL IMPROVEMENT - The improvement of the flow characteristics of a channel by clearing, excavation, realignment, lining or other means in order to increase its water carrying capacity.

CHANNEL STABILIZATION - Erosion prevention and stabilization of distribution in a channel using jetties, drops, revetments, structural linings, vegetation and other measures.

CHECK DAM - A small dam constructed in a gully or other small watercourse to decrease the stream flow velocity (by reducing the channel gradient), minimize channel scour and promote deposition of sediment.

CHUTE - A high velocity, open channel for conveying water to a lower level without erosion.

CITY ARBORIST - The City arborist, arborist plan reviewer or other designee of the Department of Environmental Protection.

CLAY (SOILS)

a.     A mineral soil separate consisting of particles less than 0.002 millimeter in equivalent diameter.

b.     A soil texture class.

c.     (Engineering) A fine grained soil (more than 50 percent passing the Number 200 sieve) that has a high plasticity index in relation to the liquid limit (Unified Soil Classification System).

COMPACTION - To unite firmly. With respect to construction work with soils, engineering compaction is any process by which the soil grains are rearranged to decrease void space and bring them into closer contact with one another, thereby increasing the weight of solid material per unit of volume, increasing the shear and bearing strength and reducing permeability.

COMPOST - A mixture of vegetable refuse, manure or other organic matter which has gone through a decaying process.

CONDUIT  - Any channel intended for the conveyance of water, whether open or closed.

CONSTRUCTION LIMIT LINE (Limit of Construction, Construction Limit, Limit Line) -  See Limits of Construction

CONTOUR

a.     An imaginary line on the surface of the earth connecting points of the elevation.

b.     A line drawn on a map connecting points of the same elevation.

CREST

a.     The top of a dam, dike, spillway or weir, frequently restricted to the overflow portion.

b.     The summit of a wave or peak of a flood.

CRITICAL AREA OR SITE  - Sediment producing, highly erodible or severely eroded areas.

CRITICAL DEPTH (HYDRAULICS) - That slope which will sustain a given discharge at uniform critical depth in a given channel.

CRITICAL ENVIRONMENTAL FEATURES - Features which have been determined to be of critical importance to the protection of one (1) or more environmental resources. They include such features as bluffs, springs, canyon rimrocks, caves, sinkholes and wetlands.

CRITICAL ROOT ZONE - The area of undisturbed natural soil around a tree defined by a concentric circle with a diameter in feet equal to twice the number of inches of trunk diameter (see Section 3.3.2 D 2).

CRITICAL WATER QUALITY ZONE - Zones along creeks and tributaries as defined in Section 25-8-92 of the Land Development Code. If a proposed development has been exempted or waived from this provision, critical water quality zones shall be those established under the applicable special watershed ordinance, if any.

CROWN  - Branch structure of a tree.

CROWN (OF SLOPE) - Top of slope, apex.

CRUSHED STONE - Aggregate consisting of angular particles produced by mechanically crushing rock.

CULM - The stem of grasses, sedges and rushes, which is jointed and usually hollow in grasses and usually solid in sedges and rushes.

CULTIPACKER - A corrugated roller used to crush sods and eliminate coarse pores in soil by firming the seed bed.

CULTIPACKER SEEDER - In addition to being a cultipacker, this is a farm tool equipped with a seed box which drops the seed between cultipacker rollers to place the seed on firm soil where they will be pressed into the soil by the second corrugated roller.

CUT - Portion of land surface or area from which earth has been removed or will be removed by excavation; the depth below original ground surface to excavated surface.

CUT-AND-FILL - Process of earth moving by excavating part of an area and using the excavated material for adjacent embankments or fill areas.

CUTOFF - A wall or other structure, such as a trench, filled with relatively impervious material intended to reduce seepage of water through porous strata.

CYCLONE (SEEDER) - A hand-turned or tractor-drawn seeder that broadcasts seed onto the seed bed by a rotary motion that slings the seed outward from the seeder.

DAM - A barrier to confine or raise water for storage or diversion, to create a hydraulic head, to prevent gully erosion or for retention of soil, sediment or other debris.

DEBRIS  - Broken remains of plants, objects and rocks that form trash or remains.

DECIDUOUS  - Plants that shed their leaves annually, as opposed to evergreen.

DEPOSITION - The accumulation of material dropped because of a slackening movement of the transporting agent, water or wind.

DESICCATION  - Drying out as of root systems of plants before they are planted.

DESILTING AREA - An area of grass, shrubs or other vegetation used for inducing deposition of silt and other debris from flowing water, located above a pond, field or other area needing protection from sediment accumulation (see filter strip).

DETENTION DAM - A dam constructed for the purpose of temporary storage of stream flow or surface runoff which releases the stored water at controlled rates.

DIAMETER - The diameter of an existing tree at 4½ feet above natural grade (diameter breast height - dbh) as determined by measuring the trunk circumference and dividing by pi (3.14) (see Figure 3-1 in Appendix V of this manual)

DIKE (ENGINEERING) - An embankment to confine or control water; for example, one built along the banks of a river to prevent overflow of lowlands; a levee.

DISTURBED AREA - An area in which the natural vegetation or soil cover has been removed or altered, which is therefore susceptible to erosion.

DIVERSION - A channel with a supporting ridge on the lower side constructed across the slope to divert water from areas where it is in excess, to sites where it can be used or disposed of safely. Diversions differ from terraces in that they are individually designed.

DOUBLE-WALLED - Constructed with more than one (1) containment layer with space between the layers sufficient to all monitoring of any leakage into or from the enclosed space. Laminated, coated or clad materials shall not be considered as double-walled construction.

DOWNTOWN AREA - For the purpose of Section 2 of this manual only, the Downtown Area shall include the Central Business District and the Downtown Mixed Use Area as established by the Land Development Code.

DRAIN (NOUN)

a.     A buried pipe or other conduit (subsurface drain).

b.     A ditch or channel (open drain) for carrying off surplus surface water or ground water.

DRAIN (VERB)

a.     To provide channels, such as open ditches or closed drains, so that excess water can be removed by surface flow or internal flow.

b.     To lose water (from the soil) by percolation.

DRAINAGE

a.     The removal of excess surface water or ground water from land by means of surface or subsurface drains.

b.     Soil characteristics that affect natural drainage.

DRAINAGE AREA (WATERSHED)  - All land and water from which runoff may run to a common (design) point.

DRIP IRRIGATION - The process of slowly applying small amounts of water on or beneath the root system of plants.

DRIPLINE - A vertical line extending downward from the outermost extremities of a tree's branches.

DROP INLET SPILLWAY - An overfall structure in which the water drops through a vertical riser connected to a discharge conduit.

DROP SPILLWAY - An overfall structure in which the water drops over a vertical wall onto an apron at a lower elevation.

DROP STRUCTURE - A structure for dropping water to a lower level and dissipating its surplus energy; a fall. The drop may be vertical or inclined.

DROUGHTY (SOIL OR SLOPE) - Lacking medium to high moisture during part of the poor growing season during a typical year.

EDWARDS AQUIFER - The water bearing substrata also known as the Edwards and Associated Limestones Aquifer. It includes the stratigraphic rock units known as the Edwards Formation and Georgetown Formation.

EDWARDS AQUIFER RECHARGE ZONE - The interim boundaries of recharge zone shall encompass all land over the Edwards Aquifer recharging the same, as determined by the surface exposure of the geologic units comprising the Edwards Aquifer, including such areas overlain with quaternary terrace deposits. Permanent boundaries may be determined at a later date as part of a more comprehensive delineation of the entire recharge zone.

EFFECTIVE SOIL  - See Topsoil.

EMERGENCY SPILLWAY - A dam spillway designed and constructed to discharge flow in excess of the principal spillway design discharge.

ENERGY DISSIPATER - A designed device, such as an apron of riprap or a concrete structure, placed at the end of a water-transmitting apparatus, such as a pipe, paved ditch or paved chute, for the purpose of reducing the velocity, energy and turbulence of the discharged water.

ENTRANCE HEAD - The height of water required to cause flow into a conduit or other structure, including both entrance loss and velocity head.

EROSION

a.     The wearing away of land surface by running water, wind, ice or other geological agents, including such processes as gravitational creep.

b.     Detachment and movement of soil or rock fragments by water, wind, ice or gravity. The following terms are used to describe different types of water erosion:

Accelerated erosion - Erosion much more rapid than normal, natural or geologic erosion, primarily as a result of the influence of the activities of man or in some cases of other animals or natural catastrophes that expose base surfaces; for example, fires.

Gully erosion - The erosion process whereby water accumulates in narrow channels and over short periods removes the soil from this narrow area to considerable depths, ranging from one (1) or two (2) feet to as much as 75 to 100 feet (see gully).

Rill erosion - An erosion process in which numerous small channels only several inches deep are formed (see rill).

Sheet erosion - The removal of a fairly uniform layer of soil from the land surface by runoff water.

Splash erosion - The spattering of small soil particles caused by the impact of raindrops on wet soils. The loosened and spattered particles may or may not be subsequently removed by surfaces runoff.

ESTHETIC (AESTHETIC) - Pleasing to look at.

EVERGREEN - Plants which have leaves or needles year long, as opposed to those that lose their leaves during part of the year.

EXCELSIOR BLANKET - An erosion retardant material made from excelsior strands held together with net-like strands of plastic or other material.

EXISTING TREE - A tree which exists on a site or easement prior to any development or disturbance.

EXISTING UNDERGROUND STORAGE TANK INSTALLATION - Any underground storage tank system in existence as of or being constructed on the effective date of the City Code or any underground storage tank installation for which a building permit was applied for prior to that date.

EXPOSURE (SLOPE).

a.     North - Slopes facing in any compass direction clockwise between N45W and S45E.

b.     South - Those slopes which face in any compass direction clockwise between S45E and N45W.

FACILITY - A building or buildings, appurtenant structures and surrounding land area used by a person at a single location or site.

FAULTS AND FRACTURES - Significant fissures or cracks in rock which may permit infiltration of surface water to underground cavities and channels.

FILTER STRIP - A strip of permanent vegetation above ponds, diversions and other structures to retard flow of runoff water, causing deposition of transported material, thereby reducing sediment flow.

FINES (SOIL) - Generally refers to the silt and clay size particles in soil.

FLOODPLAIN - The land area adjacent to a waterway necessary to contain a 100 year flood under fully developed conditions in accordance with the Drainage Criteria Manual, as well as all land contained within a Critical Water Quality Zone, where Section 25-8-92 of the Land Development Code applies.

FORBS - Vascular plants other than trees, shrubs, woody vines or grasses.

FREEBOARD (HYDRAULICS) - The vertical distance between the maximum water surface elevation anticipated in design and the top of retaining banks or structures. Freeboard is provided to prevent overtopping due to unforeseen conditions.

FRONT WALL (BUILDING) - A building wall facing and parallel to a street or a building wall facing a street at an angle less than 45 degrees.

GABION - A flexible, woven wire basket composed of two (2) to six (6) rectangular cells filled with small stones. Gabions may be assembled into many types of structures, such as revetments, retaining walls, channel liners, drop structures and groins.

GABION MATTRESS - A thin gabion, usually six (6) or nine (9) inches thick, used to line channels for erosion control.

GRADE

a.     The slope of a road, channel or natural ground.

b.     The finished surface of a canal bed, roadbed, top of embankment or bottom of excavation; any surface prepared for the support of construction, like paving or laying a conduit.

c.     To finish the surface of a canal bed, road bed, top of embankment or bottom of excavation.

GRADE STABILIZATION STRUCTURE - A structure for the purpose of stabilizing the grade of a gully or other watercourse, thereby preventing further head cutting or lowering of the channel grade.

GRASSED WATERWAY - A natural or constructed waterway, usually broad and shallow, covered with erosion-resistant grasses, to convey surface water down the slope.

GRAVEL

a.     Aggregate consisting of mixed sizes of ¼ inch to three (3) inch particles, which normally occur in or near old stream beds and have been worn smooth by the action of the water.

b.     A soil having particle sizes, according to the Unified Soil Classification System, ranging from the Number 4 sieve size (approximately ¼ inch) to three (3) inches. Particles may be natural gravel or angular in shape, as produced by mechanical crushing.

GRAVEL ENVELOPE - Selected aggregate placed around the screened or perforated pipe section of well casing or a subsurface drain to facilitate the entry of water into the well or drain.

GRAVEL FILTER - Washed and graded sand and gravel aggregate, placed around a drain or well screen to prevent the movement of fine materials from the surrounding material into the drain or well.

GROUND COVER - Plants which are low-growing and provide a thick growth which protects the soil, as well as providing some beautification of the area occupied.

GULLY - A channel or miniature valley cut by concentrated runoff through which water commonly flows only during and immediately after heavy rains. The distinction between gully and rill is one of depth. A gully is sufficiently deep enough not to be obliterated by normal tillage operations, whereas a rill is of less depth and would be smoothed by ordinary farm tillage.

HAZARDOUS MATERIAL - Any material which is subject to regulation pursuant to Chapter 9-10 of the Austin City Code.

HEAD (HYDRAULICS) -

a.     The height of water above any plane or reference.

b.     The energy, either kinetic or potential, possessed by each weight of a liquid expressed as the vertical height through which a unit weight would have to fall to release the average energy possessed. Used in various compound terms such as pressure head, velocity head and head loss.

HERBACEOUS PERENNIAL (PLANTS) - A plant whose stems die back to the ground each year.

HERBICIDE - Chemical formulations used to control weeds or brush.

HULLED (SEED) - Seed without hulls such as Sericea lespedeza. Seed are usually processed after threshing to take off outer hull to facilitate scarification and quicken germination.

HYDRAULIC GRADE LINE - In a closed conduit, a line joining the elevations to which water could stand in risers or vertical pipes connected to the conduit at their lower end and open at their upper end. In open channel flow, the hydraulic grade lien is the free water surface.

HYDRAULIC GRADIENT - The slope of the hydraulic grade line. The slope of the free surface of water flowing in an open channel.

HYDRAULIC JUMP - The sudden turbulent rise in water level from a flow stage below critical depth to flow stage above critical depth, during which the velocity passes from super critical to subcritical.

HYDRAULIC RADIUS - The cross-sectional area of a channel divided by its wetted perimeter. The "r" in Manning's Formula.

HYDROGRAPH - A graph showing variation in stage (depth) or discharge of a stream of water over a period of time.

HYDROSEEDER - A machine designed to apply seed, fertilizer, lime and short fiber wood or paper mulch to the soil surface.

HYDROSEEDING  - Seeding with a hydroseeder.

INLET (HYDRAULICS) -

a.     A surface connection to a closed drain.

b.     A structure at the entrance end of a conduit.

c.     The upstream end of any structure through which water may flow.

IN-CHANNEL DETENTION - Detention accomplished by channel storage or onstream storage, as opposed to offstream or upland detention (see the Drainage Criteria Manual).

INSTALLED TREE  - A tree which is planted on a site after development occurs.

INTERCEPTOR DRAIN - A surface or subsurface drain or a combination of designed and installed to intercept flowing water.

IRRIGATION - Providing water to plants in an amount and frequency adequate to sustain growth of the plants on a permanent basis.

ISOBUTYLIDENE UREA - A slowly soluble synthetic organic compound containing 31 percent nitrogen.

ISOLATED BUILDING - A detached building in front of and physically separate from the main building or buildings on a site and smaller in square footage than the anchor building.

JUTE - A coarsely woven material of jute yarn which can be used to control soil erosion in waterways and on steep slopes.

KARST FEATURE - For the purpose of these guidelines a karst feature is defined as a cave, fault, fracture, joint, sinkhole or other associated features formed in limestone, dolomite or associated geologic strata.

LANDSCAPE AREA - Any area within the boundaries of a given lot which is devoted to and consists of living plant material and other landscape material, including but not limited to grass, trees, shrubs, flowers, vines, groundcover, native plant materials, existing native vegetation areas, planters, brick, stone, natural forms, water forms and other landscape features, but not including the use of smooth concrete, asphalt or aggregate. Provided, however that the use of nonliving landscape materials shall not predominate over the use of organic living plant material within any single landscape area.

LANDSCAPE ISLAND - A landscape area completely surrounded by a parking area and/or a vehicular use area.

LANDSCAPE MEDIAN - A linear landscape area between two (2) rows of parking, between two (2) drives or between a row of parking and a drive.

LANDSCAPE PENINSULA - A landscape area surrounded on two (2) or three (3) sides by a parking area and/or a vehicular use area.

LARGE SHRUB - A woody plant of smaller proportions than a tree which usually produces several branches from the base and will reach a mature height of over four (4) feet.

LARGE TREE  - A tree species listed in Appendix F as having a mature height of more than 30 feet.

LAYERING  - A shoot or twig attached to the living stock for the purpose of propagation.

LIME - Basic calcareous materials used to raise pH of acid soils for benefit of plants being grown. May be either ground limestone or hydrated lime.

LIMITS OF CONSTRUCTION - The outer limits of the area which will be disturbed by a proposed development activity including the area of all proposed cuts, fills, regrading, structures, ancillary facilities, temporary utilities, temporary or permanent spoil storage areas, access roads, storage areas, staging areas and any other activities or facilities which may cause temporary or permanent loss or damage of vegetation or disruption of the soil surface.

LINEAMENT - A linear figure that is perceived from an aerial photograph of a site, is continuous with definable end points and lateral boundaries, has a relatively high length/width ratio and hence a discernible azimuth and is shown or presumed to be correlated with natural structural geological features.

LINEAR DEVELOPMENT - Development which is typically not confined to one site and is linear in nature such as a utility or waterway alteration project.

MANNING'S FORMULA (HYDRAULICS) - A formula used to predict the velocity of water flow in an open channel or a pipeline:

V = 1.486 R2/3 S1/2
                n

Wherein V is the mean velocity of flow in feet per second; R is the hydraulic radius; S is the slope of the energy gradient or for assumed uniform flow the slope of the channel, in feet per foot; and n is the roughness coefficient or retardance factor of the channel lining.

MEDIUM SHRUB - A woody plant of smaller proportions than a tree which usually produces several branches from the base and will have a maximum mature height of between four (4) and six (6) feet.

MULCH - Covering on surface of soil to protect and enhance certain characteristics, such as water retention qualities.

MULCH ANCHORING TOOL - A tool that looks like a dull disk designed to press straw and similar mulches into the soil to prevent loss due to wind, water or gravity.

NATIVE PLANTS - Plants native to the Austin area or adjacent areas of the Edwards Plateau, which are compatible with environmental conditions of a site or portions of a site. The standard reference for this criterion shall be the Manual of Vascular Plants of Texas by Correll and Johnston, published by the University of Texas at Dallas (1970).

NATURAL AREA  - Area of a site existing in a natural state.

NATURAL FORMS - Features in a natural landscape other than plants, such as ponds, streams, rock outcroppings, cliffs, etc.

NATURAL GROUND  - Ground surface which has not been disturbed by man.

NATURAL GROUND COVER - Any organic material either existing prior to construction or installed after construction.

NATURAL STATE - Substantially the same conditions of the land which existed prior to any development, including, but not limited to, the same type, quality, quantity and distribution of soils, ground cover, vegetation and topographic features.

NETTING (MULCH)  - Plastic, paper or cotton material used to hold mulch material on the soil surface.

NEW UNDERGROUND STORAGE TANK INSTALLATION - Any underground storage tank installation for which a building permit was applied for after the effective date of this article or any existing underground storage tank installation which is substantially modified or added to after that date.

NITROGEN-FIXING (BACTERIA) - Bacteria having the ability to fix atmospheric nitrogen, making it available for use by plants. Inoculation of legume seeds is one way to insure a source of these bacteria for specified legumes.

NORMAL DEPTH - Depth of flow in an open conduit during uniform flow for the given conditions (see uniform flow).

NOXIOUS WEEDS - Harmful; undesirable; hard to control.

a.     Restricted - may be sold in the trade, but are limited to very small amounts as undesirable contaminants.

OFFICER - The employee assigned by the City to administer the City Code or the designee of such employee, who shall also be a City employee.

OUTFALL - The point where water flows from a conduit, stream or drain.

OUTLET - The point at which water discharges from such things as a stream, river, lake, tidal basin, pipe, channel or drainage area.

OUTLET CHANNEL - A waterway constructed or altered primarily to carry water from manmade structures, such as terraces, subsurface drains, diversions and impoundments.

OVATE  - Egg-shaped in outline.

OVERBANK - The area outside the immediate natural stream channel or outside the pilot channel of a new channel which contains the 100 year floodplain.

OVERFALL - Abrupt change in stream channel elevation; the part of a dam or weir notch over which the water flows.

OVOID  - A three (3) dimensional solid, ovate in outline.

PADS - Individual pieces of sod cut to supplier's standard width and length.

PAPER FIBER - A short fiber mulch material usually applied by hydroseeder along with fertilizer and seed.

PARENT MATERIAL  - The unconsolidated rock material from which the soil profile develops.

PARKING BAY - A parking area serviced by one (1) drive and including back-up space. This may include a single bay with one (1) row of parking or a double bay with two (2) rows of parking sharing a common drive.

PARKING STRUCTURE - Any parking area which is totally or partially enclosed overhead or in which the parking surface is not at finish grade.

PERMANENT SEEDING - Results in establishing perennial vegetation which may remain on the area for many years.

PERMANENT STORAGE OR PERMANENTLY STORING - Shall mean storage for a period of over thirty (30) days.

PERMEABLE PAVING - A paving surface which permits adequate gas exchange and water penetration to sustain a tree root system beneath it.

PERMISSIBLE VELOCITY (HYDRAULICS) - The highest average velocity at which water may be carried safely in a channel or other conduit. The highest velocity that can exist through a substantial length of a conduit and not cause scour of the channel. Safe, noneroding or allowable velocity.

PERMIT - Any Hazardous Material Underground Storage Tank Registration Permit issued pursuant to the City Code.

PERMITTEE - Any person to which a permit is issued pursuant to the City Code and any authorized representative, agent or designee of such person.

PERSON - Any individual, firm, trust, partnership, corporation, joint venture, association or other legal entity; any group of the foregoing, organized or united for a business purpose; or any governmental entity.

pH - A number denoting the common logarithm of the reciprocal of the hydrogen ion concentration. A pH of seven (7.0) denotes neutrality, higher values indicate alkalinity and lower values indicate acidity.

PHREATIC LINE - The upper surface of the zone of saturation in an embankment is the phreatic (zero pressure) surface; in cross section, this is called the phreatic line.

PIPES OR PIPING - Any pipeline system which is used for the transfer of hazardous materials in connection with an underground storage tank within the confines of a facility.

PIPING - Removal of soil material through subsurface flow channels or "pipes" developed by seepage water.

PLANT MATERIALS  - Living plants which are part of an installed landscape.

PLASTICITY INDEX - See Atterberg limits.

PLASTIC LIMIT - See Atterberg limits.

PLUGS - Pieces of turf or sod, usually cut with a round tube, which can be used to propagate the turf or sod by vegetative means.

POINT RECHARGE FEATURE - Any cave, sinkhole, fault, joint or other specific natural feature situated over the Edwards Aquifer Recharge Zone which may be demonstrated to transmit, or has the potential to transmit, a significant amount of surface water into the subsurface strata.

PRECISION TEST - Any test performed on an underground storage tank system which is capable of measuring a quantitative leak rate and which controls, eliminates, measures or otherwise takes into account changes in the coefficient of expansion of the liquid due to temperature changes, containment system deformations due to pressure changes, evaporative losses and other relevant variables during the course of the test, as discussed in NFPA 329, "Recommended Practice for Handling Underground Leakage of Flammable and Combustible Liquids," as amended and published by the National Fire Protection Association.

PRESS WHEEL - A wheel which usually follows a seeding and presses seed into or on the surface of the seed bed.

PRIMARY CONTAINMENT - The first level of containment or the inside portion of an underground storage tank system, which comes into immediate contact on its inner surface with hazardous material being contained, including the piping.

PROCUMBENT  - Lying down prone; trailing as a vine, usually not rooting at the nodes.

PRODUCT TIGHT - Impervious to the hazardous material which is contained so as to prevent the release of the hazardous material from the primary containment. To be product tight, the tank shall be made of a material that is highly resistant to physical or chemical deterioration by the environment and the hazardous material being contained or shall be equipped with an inner liner which protects the construction material of the tank from the environment and the contained material.

PROTECTED RIPARIAN AREAS - Those ecological features within a floodplain associated with a waterway segment, which contribute to the natural and traditional character of the waterway, as follows:

1.     Floodplain woodlands. Any wooded area in a floodplain with all of the following characteristics:

•     Has a minimum extent of canopy cover of ½ acre;

•     Voids in the canopy cover comprise less than 30 percent of the total woodland area;

•     At least 50 percent of all trees which have diameters of eight (8) inches or greater measured at 4½ feet above the ground are comprised of three (3) or more of the following species:

pecan                         Carya illinoiensis
          American elm                    Ulmus americana
          Arizona walnut                    Juglans major
          bald cypress                    Taxodium distichum
          black walnut                    Juglans nigra
            bur oak                    Quercus macrocarpa
          cedar elm                    Ulmus crassifolia
          little walnut                    Juglans microcarpa
          green ash                    Fraxinus pennsylvanica
          Texas sugarberry               Celtis laevigata
          American sycamore               Platanus occidentalis
          Eastern cottonwood               Populus deltoides
          Black willow                    Salix nigra

2.     Wetlands (other than springs). As defined in Section 25-8-1 of the Land Development Code.

3.     Permanent natural pools in perennial or intermittent waterways.

PROTECTED TREE - A tree having a trunk circumference of 60 inches or more, measured at 4½ feet above natural grade level.

QUALIFIED PERSON - Experienced as defined in A.P.I. (American Petroleum Institute) Bulletin 1631, 1987 edition.

RELEASE - Any spilling, leaking, emitting, discharging, escaping, leaching or disposing into ground water, surface water or soils.

RESIDUES (PLANT) - Dead parts of plants which may be left on the soil surface following harvest, grazing or cutting.

RESTORATION  (See Revegetation)

RETENTION - The amount of precipitation on a drainage area that does not escape as runoff. It is the difference between total precipitation and total runoff.

REVEGETATION - The installation of native trees, shrubs, grasses and wildflowers in an area after its disturbance, along with subsequent maintenance, intended to restore the area to a natural state.

REVETMENT - Facing of stone or other materials, either permanent or temporary, placed along the edge of a stream or shoreline to stabilize the bank and to protect it from the erosive action of water.

RHIZOME - Any prostate, more or less elongated stem growing partly or completely beneath the surface of the ground; usually rooting at the nodes and becoming upcurved at the apex.

RIGHT OF WAY - Right of passage, as over another's property. A route that is lawful to use. A strip of land acquired for transport or utility construction.

RILL - A small channel cut by concentrated runoff, but through which water commonly flows only during and immediately after rains. A rill is usually only a few inches deep (but no more than one (1) foot) and hence, no obstacle to tillage operations.

RIPPING - Pulling a chisel or subsoiling implement through the soil to reduce compaction and promote infiltration of water into the soil. Does not invert the soil.

RIPRAP - Broken rock, cobbles or boulders placed on earth surfaces, such as the face of a dam or the bank of a stream, for protection against the action of water (waves); also applies to brush or pole mattresses or brush and stone or similar materials used for soil erosion control.

ROUGHNESS COEFFICIENT (HYDRAULICS) - A factor in velocity and discharge formulas representing the effect of channel roughness on energy losses in flowing water. Manning's "n" is a commonly used roughness coefficient.

RUNOFF (HYDRAULICS) - That portion of the precipitation on a drainage area that is discharged from the area in stream channels. Types include surface runoff, ground water runoff or seepage.

SAND

a.      (Agronomy) A soil particle between 0.05 and 2.0 millimeters in diameter.

b.     A soil textural class.

c.     (Engineering) According to the Unified Soil Classification System, a soil particle larger than the Number 200 sieve (0.074 millimeters) and passing the Number 4 sieve (approximately ¼ inch).

SCREENED - Shielded, concealed and effectively hidden from the view of a person standing at ground level on an abutting site or outside the area or feature so screened, by a fence, wall, hedge, berm or similar architectural or landscape feature which is, or will grow to, at least six (6) feet in height.

SECONDARY CONTAINMENT - The level of containment external to, and separate from, the primary containment, consisting of an impervious layer of materials which are installed so that any release of hazardous materials from the primary containment of an underground storage tank installation will be prevented from contacting the environment outside said impervious layer.

SEDIMENT - Solid material, both mineral and organic, that is in suspension, is being transported or has been moved from its site of origin by air, water, gravity or ice and has come to rest on the earth's surface either above or below sea level.

SEDIMENTATION  - Deposition of detached soil particles.

SEDIMENT DISCHARGE (SEDIMENT LOAD) - The quantity of sediment, measured in dry weight or by volume, transported through a stream cross section in a given time. Sediment discharge consists of both suspended load and bedload.

SEEPAGE

a.     Water escaping through or emerging from the ground.

b.     The process by which water percolates through the soil.

SEEPAGE LENGTH - In sediment basins or ponds, the length along the pipe and around the antiseep collars that is within the seepage zone through an embankment (see phreatic line).

SHEET FLOW - Water, usually storm runoff, flowing in a thin layer over the ground surfaces.

SIDE SLOPES (ENGINEERING) - The slope of the sides of a canal, dam or embankment. It is customary to name the horizontal distance first, as 1.5:1 meaning a horizontal distance of 1.5 feet to one (1) foot vertical.

SIDE WALL (Building) - A building wall perpendicular to a street; a building wall facing a street at an angle of more than 45 degrees.

SIGNIFICANT TREE - A tree determined to be significant by the Department of Environmental Protection using the tree evaluation method described in Section 3.5.1.

SILT -

a.     (Agronomy) A soil separate consisting of particles between 0.05 and 0.002 millimeter in equivalent diameter.

b.     A soil textural class.

c.     (Engineering) According to the Unified Soil Classification System, a fine grained soil (more than 50 percent passing the Number 200 sieve) that has a low plasticity index in relation to the liquid limit.

SINGLE-WALLED - Constructed with walls made of but one (1) thickness of material. Laminated, coated or clad materials shall be considered as single-walled construction.

SINKHOLE - A circular or oblong depression formed in soluble rock by the action of subterranean water which is a potential point of significant recharge.

SITE SPECIFIC DEVELOPMENT - Development which is typically confined to one (1) lot and is not linear in nature.

SLURRY - A thickened, aqueous mixture of such things as seed, fertilizer, short fiber mulch or soil.

SMALL GRAIN MULCH MATERIAL  - Straw material from oats, barley, wheat or rye.

SMALL SHRUB - A woody plant of smaller proportions than a tree which usually produces several branches from the base and will have a maximum mature height of between two (2) and four (4) feet.

SMALL TREE  - A tree species listed in Appendix F as having a mature height of 30 feet or less.

SOD  - A piece of earth containing grass plants with their matted roots; turf.

SODDED WATERWAY  - A grassed waterway vegetated by sodding with adapted species of grasses.

SOIL

a.     (Agronomy) The unconsolidated mineral and organic material on the immediate surface of the earth that serves as a natural medium for the growth of land plants.

b.     (Engineering) Earth and rock particles resulting from the physical and chemical disintegration of rocks and may or may not contain organic matter. It includes fine material (silts and clays), sand and gravel.

SOIL TEST - Chemical analysis of soil to determine needs for fertilizers or amendments for species of plants being grown.

SPECIFIC ENERGY - The energy of a stream referred to its bed, namely, depth plus velocity head of mean velocity.

SPILLWAY - An open or closed channel or both, used to convey excess water from reservoir. It may contain gates, either manually or automatically controlled, to regulate the discharge of excess water.

SPREADER (HYDRAULICS)  - A device for distributing water uniformly in or from a channel.

STABILIZATION - Providing adequate measures, vegetative and/or structural, that will prevent erosion from occurring.

STABILIZED AREA - An area sufficiently covered by erosion resistant material, such as a good cover of grass or paving by asphalt, concrete or stone, in order that erosion of the underlying soil does not occur.

STABILIZED GRADE  - The slope of a channel at which neither erosion nor deposition occurs.

STABLE (STREAM OR CHANNEL) - The condition of a stream, channel or other water course in which no erosion or deposition occurs; adequately protected from erosion.

STAGE (HYDRAULICS)  - The variable water surface or the water surface elevation above any chosen datum.

STATIC HEAD - Head resulting from elevation difference; for example, the difference in elevation in headwater and tailwater in a hydroelectric plant.

STILLING BASIN - An open structure or excavation at the foot of an overfall, conduit, chute, drop or spillway to reduce the energy of the descending stream of water.

STOLON - A trailing or reclining above ground stem capable of rooting and/or sending up new shoots from the nodes.

STORAGE TANK - Any tank, sump, vault or other containment vessel which has a primary storage capacity of 60 gallons or more.

STREET VIEW - The view into a site from any point on an adjacent street or roadway.

STREET YARD - The street yard is the area of a lot which lies between the street right of way line and the actual front wall line of the building, as such building wall line extends from the outward corners of the building parallel to the street, until such imaginary extensions of such front building wall line intersects the side property lines.

STRUCTURAL - Relating to something constructed or built by man.

STRUCTURE (SOIL) - The combination or arrangement of primary soil particles into secondary particles, units or pads.

SUBCRITICAL FLOW  - Flow at velocities less than critical velocity.

SUBGRADE  - The soil prepared and compacted to support a structure or a pavement system.

SUBSOIL - Roughly, that part of the soil below plow depth.

SUMP - A pit or well in which liquids collect.

SUMPAGE - Water that enters a primary or secondary containment system other than by direct precipitation or runoff.

TAILWATER (HYDRAULICS) - Water in a river or channel immediately downstream from a structure.

TANK INSTALLATION - Any one (1) or combination of storage tank systems.

TANK SYSTEM - A storage tank and all piping and appurtenances in connection with it which is used for the storage, transfer or containment of hazardous materials at a facility.

TEMPORARY SEEDING - A seeding which is made to provide temporary cover from the soil while waiting for further construction or other activity to take place.

TERRACE - An embankment or combination of an embankment and channel constructed across a slope at a suitable spacing to control erosion by diverting or storing surface runoff instead of permitting it to flow uninterrupted down the slope. Normally used only on cropland.

TEXTURE (SOIL) - The relative proportions of various soil separates in a soil material.

THATCH - A tightly intermingled layer of living and dead stems, leaves and roots of grasses.

THREAT TO HUMAN LIFE  - For purposes of these guidelines, a threat to human life exists when either or both of the following conditions exist:

a.     Occupied Structures. The water surface elevation of the 100 year flood is greater than the lowest habitable finished floor elevation and/or the water velocity at the perimeter of the structure exceeds three (3) feet per second.

b.     Roadway Crossings (rights of way). The water surface of the 100 year flood results in residential roadway flooding exceeding 12 inches above the roadway crown or exceeding six (6) inches above the crown for roadways larger than residential.

TIME OF CONCENTRATION - Time required for water to flow from the most remote point of a watershed in a hydraulic sense to the outlet.

TOE (OF SLOPE)  - Where the slope stops or levels out. The bottom of the slope.

TOE WALL - The downstream wall of a structure, usually to prevent flowing water from eroding under the structure

TOPSOIL

a.     Presumably fertile or desirable soil material used to top dress road banks, subsoils, parent material, etc.

b.     Effective Soil - Surface soils which contain a variable mixture of weathered minerals, organic matter and in some cases, coarse fragments. The effective topsoil volume includes only that portion of the total volume which is the fine earth fraction (<two (2.0) mm in diameter grain size). This soil zone reflects the area of major root development, bacterial activity, cation exchange and physical filtration.

TRAP EFFICIENCY - The capability of a reservoir to trap sediment. The ratio of sediment trapped to the sediment delivered, usually expressed in percent.

TRASH RACK - Grill, grate or other device at the intake of a channel, pipe, drain or spillway for the purpose of preventing oversize debris from entering the structure.

TREE CLUSTERS - A group of three (3) or more trees with trunk diameters ranging from two (2) to six (6) inches which can be enclosed in a circle with a radius of ten (10) feet (see Figure 3-4 in Appendix V of this manual).

TREE REMOVAL - The uprooting or severing of the main trunk of a tree or any act which causes or may reasonably be expected to cause a tree to die, including, but not limited to, damage inflicted upon the root system by machinery, storage of materials or soil compaction; substantially changing the natural grade above the root system or around the trunk; excessive pruning or paving with concrete, asphalt or other impervious materials in a manner which may reasonably be expected to kill a tree.

TUFTS - Having a cluster of hairs or other slender outgrowths; stems in a very close cluster.

UNDERGROUND STORAGE TANK - That portion of a storage tank system which has its available primary containment volume beneath the final cover and is surrounded by a backfill material.

UNHULLED (SEED) - Seed still encased with a hull. Example: Sericea lespedza before it is rendered hulless by mechanically removing the hull.

UNIFIED SOIL CLASSIFICATION SYSTEM (ENGINEERING) - A classification system based on the identification of soils according to their particle size, gradation, plasticity index and liquid limit.

UNIFORM FLOW - A state of steady flow when the mean velocity and cross sectional area are equal at all sections of a reach.

UNIVERSAL SOIL LOSS EQUATION - An equation used for the design of water erosion control system: A = RKLSCP, wherein "A" is average annual soil loss in tons per acre per year; "R" is rainfall factor; "K" is soil erodibility factor; "L" is length of slope; "S" is percent of slope; “C" is cropping and management factor; and "P" is conservation practice factor.

UPLIFT (HYDRAULICS)  - The upward force of water on the base or underside of a structure.

UREAFORM-URAMITE/UREAFORMALDEHYDE - A slowly soluble synthetic organic fertilizer containing 38 percent nitrogen, which contains about 30 percent readily available nitrogen.

VARIETY  - A variant within a species which reproduces true by seed or vegetative propagation as applicable.

VEHICULAR USE AREAS - Areas of a site used for the movement or other operation of vehicles, such as drives, loading docks, fire lanes, etc.

VELOCITY HEAD (HYDRAULICS) - Head due to the velocity of a moving fluid, equal to the square of the mean velocity divided by twice the acceleration due to gravity (32.16 feet per second).

WATER SUPPLY RURAL WATERSHEDS - All watersheds which are incorporated by reference herein, including all land within the City of Austin's jurisdiction and draining to: Lake Austin (excluding areas on the east side of the lake south of and including Bull Creek), Lake Travis, Little Barton Creek, Barton Creek (excluding the area east of Barton Creek and north of Loop 360) and the portions of the Onion, Bear, Little Bear and Slaughter Creek Watersheds (upstream of FM 1826) which are located in the Edwards Aquifer Recharge or Contributing Zones.

WATER SUPPLY SUBURBAN WATERSHEDS - All watersheds which are incorporated by reference herein including all land within the City of Austin's jurisdiction and draining to: Barton Creek (east of Barton Creek and north of Loop 360), Bull, West Bull, Dry (North and West), Taylor Slough, Lake and Rattan Creeks, Town Lake (south side from Barton Creek to Tom Miller Dam), Town Lake (north side from Johnson Creek to Tom Miller Dam), other Lake Austin (east side from Tom Miller Dam to Bull Creek) and those portions of the Williamson, Slaughter (downstream of FM 1826) and Brushy Creek Watersheds which are located in the Edwards Aquifer Recharge or Contributing Zones.

WATER SURFACE PROFILE (HYDRAULICS) - The longitudinal profile assumed by the surface of a stream flowing in an open channel; the hydraulic grade line.

WATERWAY - As defined in Section 9-10-1 of the Austin City Code for areas within the City or as defined in Section 25-8-1 of the Land Development Code for areas within the extraterritorial jurisdiction of the City. In urban watersheds exempt from Chapter 25-8 but subject to Chapter 9-10, only waterways draining a tributary area of at least 128 acres shall be evaluated under these guidelines.

WEEP-HOLES (ENGINEERING) - Openings left in retaining walls, aprons, linings or foundations to permit drainage and reduce pressure.

WETTED PERIMETER (HYDRAULICS) - The length of the line of intersection of the plan of the hydraulic cross section with the wetted surface of the channel.

WING-WALL - Side wall extensions of a structure used to prevent sloughing of banks or channels and to direct and confine overfall.

WINTERKILL - Killed by low temperatures during winter months.

WOOD FIBER  - A short fiber mulch material, usually applied with a hydroseeder in an aqueous mixture.

XERISCAPE - A method of landscaping using certain principles of design and installation which conserve water and energy.

Disclaimer:
The Technical Criteria Manuals and/or any other documents that appear on this site may not reflect the most current legislation adopted by the City of Austin, Texas. American Legal Publishing Corporation provides these manuals for informational purposes only. These manuals should not be relied upon as the definitive authority for local legislation. Additionally, the formatting and pagination of the posted documents varies from the formatting and pagination of the official copy. The official printed copy of the Technical Criteria Manuals should be consulted prior to any action being taken.

For further information regarding the official versions of the Technical Criteria Manuals or other documents posted on this site, please contact the City of Austin, Texas directly or contact American Legal Publishing toll-free at 800-445-5588.

© 2002 American Legal Publishing Corporation

techsupport@amlegal.com

1.800.445.5588.